## Slide 1
Lab Book 0.2. Couplers
Student:

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/pic-upv-lab0.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  020_COUPLERS_Student.ipynb
Cross-Sections to be studied:
h
(height)
w (width)
Core
Cladding
w (width)
MMI Body
Cladding
Multimode Interference (MMI) coupler
Directional coupler (DC)
Core
g
(gap)
h
(height)

## Slide 3: Learning outcome #1 – Directional coupler cross-section in GDSFactory
INSTRUCTOR:
Present Python and GDSFactory implementation of DC cross-section
Describe how to obtain the beating length
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, gap between waveguides 0.6 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 4: Learning outcome #2 – Multimode Interference (MMI) Coupler cross-section
INSTRUCTOR:
Present Python and GDSFactory implementation of DC cross-section
Describe how to obtain the beating length
Describe the outputs.
ALL EXAMPLE #2: waveguide width 12 µm, gap between waveguides 0.6 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 5: Learning outcome #2 – Multimode Interference (MMI) Coupler cross-section
Notes: Mencionar que a medida que incrementa el ancho de la guía se incrementa el numero de modos que se propaga a través de la misma, una forma practica de conocer el numero de modos es llevar a cabo las simulaciones de su índice efectivo y verificar el punto en los que estos comienzan a acercarse al índice efectivo del cladding, podríamos afirmar que a partir del modo 23 comienza a acercarse al índice de refracción del silicio de 1,45

## Slide 6: Thank you